OpenAirInterface for SystemX
# Source code, Compilation
## How to use Openairinterface source code
...
## Terminology
This document use the 5G terminology
Central Unit (CU): It is a logical node that includes the gNB functions like Transfer of user data, Mobility control, Radio access network sharing, Positioning, Session Management etc., except those functions allocated exclusively to the DU. CU controls the operation of DUs over front-haul (Fs) interface. A central unit (CU) may also be known as BBU/REC/RCC/C-RAN/V-RAN/VNF
Distributed Unit (DU): This logical node includes a subset of the gNB functions, depending on the functional split option. Its operation is controlled by the CU. Distributed Unit (DU) also known with other names like RRH/RRU/RE/RU/PNF.

In OpenAir code, the terminology is often RU and BBU.
# Usage
## EPC and general environment
### OAI EPC
Use the stable OAI EPC, that can run in one machine (VM or standalone)
Draft description: https://open-cells.com/index.php/2017/08/22/all-in-one-openairinterface-august-22nd/
## Standalone 4G
EPC+eNB on one machine, the UE can be commercial or OAI UE.
### USRP B210
Main current issue: traffic is good only on coaxial link between UE and eNB (probably power management issue).

### Simulated RF
Running eNB+UE both OAI can be done over a virtual RF link.
The UE current status is that threads synchronization is implicit in some cases. As the RF simulator is very quick, a “sleep()” is required in the UE main loop
(line 1744, targets/RT/USER/lte-ue.c).
Running also the UE in the same machine is possible with simulated RF.
Running in same machine is simpler, offers about infinite speed for virtual RF samples transmission.
A specific configuration is required because the EPC Sgi interface has the same IP tunnel end point as the UE.
So, we have to create a network namespace for the UE and to route data in/out of the namespace.

ip netns delete aNameSpace 2> /dev/null
ip link delete v-eth1 2> /dev/null

ip netns add aNameSpace
ip link add v-eth1 type veth peer name v-peer1
ip link set v-peer1 netns aNameSpace
ip addr add 10.200.1.1/24 dev v-eth1
ip link set v-eth1 up
iptables -t nat -A POSTROUTING -s 10.200.1.0/255.255.255.0 -o enp0s31f6 -j MASQUERADE
iptables -A FORWARD -i enp0s31f6 -o v-eth1 -j ACCEPT
iptables -A FORWARD -o enp0s31f6 -i v-eth1 -j ACCEPT

ip netns exec aNameSpace ip link set dev lo up
ip netns exec aNameSpace ip addr add 10.200.1.2/24 dev v-peer1
ip netns exec aNameSpace ip link set v-peer1 up
ip netns exec aNameSpace bash
After the last command, the Linux shell is in the new namespace, ready to run the UE.
To make user plan traffic, the traffic generator has to run in the same namespace
ip netns exec aNameSpace bash
The traffic genenrator has to specify the interface:
route add default oaitun_ue1
or specify the outgoing route in the traffic generator (like option “-I” in ping command).
## Split 6 DL 4G
The contract describes to reuse the uplink existing if4p5 and to develop is this work the downlink “functional split 6”.
The customer required after signature to develop also the uplink functional split 6. This is accepted, as long as the whole work is research with no delivery completeness warranty.
### Simulation
To be able to verify the new features and to help in all future developments, Open Cells added and improved the Rf board simulator during this contract.
We added the channel modeling simulation, that offer to simulate various 3GPP defined channels.
### Main loop cleanup
The main log is in RF simulator is in
 targets/RT/USER/lte-ru.c and targets/RT/USER/lte-enb.c
As this piece of SW is very complex and doesn’t meet our goals (functional split 6), a cleaned version replaces these 2 files in executables/ocp-main.c (openair1/SCHED/prach_procedures.c is also replaced by this new file as it only launching the RACH actual work in a way not compatible with our FS6).
The main loop cadences the I/Q samples reception, signal processing and I/Q samples sending.
The main loop uses extensively function pointers to call the right processing function depending on the split case.
This is enough for RF board dialog, but the FS6 is higher in SW layers, we need to cut higher functions inside downlink and uplink procedures.
### General design of the FS6 split
A transport layer allows to send/receive blocks of data. It uses a compact header to enable multi-UDP packets association
This transport is used by CU and DU in each direction: UL and DL.
The CU/DU adds a second header in each UDP packet to make redundancy of information that is mandatory for the whole subframe.
It adds then data per UE in each packet (if one packet is lost, the received paquets can be processed).
All headers are in split_headers.h file.
### Main loops for FS6 CU and DU
The source is in executables/main-fs6.c
Cu_fs6() and du_fs6() are the two main loops.
Each of these main loops do:
- initialize the LTE configuration values for the eNB made of this CU/DU
- the du loads the RF board driver
- CU and DU opens the UDP socket that links them
- DU loops on
  - UL_du_fs6()
  - DL_du_fs6()
- CU loops on
  - UL_cu_fs6()
  - DL_cu_fs6()
### DownLink
The main procedure is phy_procedures_eNB_TX
This is building the common channels (beacon, multi-UE signaling).
The FS6 split breaks this function into pieces:
- The multi-UE signals, built by common_signal_procedures(), subframe2harq_pid(), generate_dci_top(), subframe2harq_pid()
  - These functions will be executed in the RU, nevertheless all context has to be sent (it is also needed partially for UL spitting)
  - IT should be in the RU also to meet the requirement of pushing in RU the data encoded with large redundancy (>3 redundancy)
- the per UE data: pdsch_procedures() that needs further splitting:
  - dlsch_encoding_all() that makes the encoding: turbo code and lte_rate_matching_turbo() that will be in the DU (some unlikely cases can reach redundancy up to x3, when MCS is very low (negative SINR cases)).
    - dlsch_encoding() output needs to be transmitted between the DU and the RU for functional split 6.
  - dlsch_scrambling() that will go in the RU
  - dlsch_modulation() that will go in the RU
### Uplink
The uplink require configuration that is part of the DL transmission.
Ocp-main.c:rxtx() calls directly the entry procedure phy_procedures_eNB_uespec_RX() calls:
- rx_ulsch() that demodulate and extract soft bits per UE.
  - This function runs in the RU
  - the output data will be processes in the DU, so it needs to be transmitted to the DU
- ulsch_decoding() that do lte_rate_matching_turbo_rx() sub_block_deinterleaving_turbo() then turbo decode
  - it runs
- fill_ulsch_cqi_indication()
  - TBD: either runs in DU or output needs to be transmitted to DU
- fill_crc_indication() , fill_rx_indication() results need also to be transmitted or made in the DU
In split mode, the DU:
- calls rx_rf()
- process the RACH symbols to detect UE entry
- phy_procedures_eNB_uespec_RX_extract() to perform the DU part of phy_procedures_eNB_uespec() (uespec=> UE specific, per UE processing).
In split mode, the CU do:
- receive data from DU
- prach_eNB_process() to process UE entry (if any)
- phy_procedures_eNB_uespec_RX_process() to perform the uppper part of phy_procedures_eNB_uespec()
### UDP transport layer
A general UDP transport layer is in executables/transport_split.c
Linux offers a UDP socket builtin timeout, that we use.
In and out buffers are memory zones that contains compacted (concatenated) UDP chunks.
For output, sendSubFrame() sends each UDP chunk
For input, receiveSubFrame() collects all UDP chunks for a group (a subframe in OAI LTE case). It returns in the following cases:
- all chunks are received
- a timeout expired
- a chunk from the next subframe already arrived
### Functional split 6 usage
The ocp cleaned main hale to be used: run oc-softmodem instead of lte-softmodem.
The functionality and parameters is the same, enhanced with FS6 mode.

The environment variable “fs6” enables the fs6 mode and decided to be cu or du from the fs6 variable content.

Example:
fs6=cu ./ocp-softmodem -O … (regular lte-softmodem paramters)
Run the CU init of the split 6 eNB.

CU and DU IP address and port are configurable in the eNB configuration file (as X2, GTP, … interfaces).
## 5G and F1
Today 5G achievement is limited to physical layer.
The available modulation is 40MHz, that require one X310 or N300 for the gNB and a X310 or N300 for the nrUE.
### Usage with X310
Linux configuration: https://files.ettus.com/manual/page_usrp_x3x0_config.html
We included most of this configuration included in OAI source code.
Remain to set the NIC (network interface card) MTU to 9000 (jumbo frames).
### Running 5G
Usage with RFsimulator:
gNB
sudo RFSIMULATOR=server ./nr-softmodem -O ../../../targets/PROJECTS/GENERIC-LTE-EPC/CONF/gnb.band78.tm1.106PRB.usrpn300.conf --parallel-config PARALLEL_SINGLE_THREAD
nrUE
sudo RFSIMULATOR=127.0.0.1 ./nr-uesoftmodem --numerology 1 -r 106 -C 3510000000 -d